## Slide 1: Transport Protocols in the Internet
Overview & Essential of UDP
IN2140: Introduction to Operating Systems and Data Communication

## Slide 2: Transport Layer Function
Transport layer tasks
1-2
3
4
5
Network
Layer
Application
Transport
Layer
1-2
3
4
5
Network
Layer
Application
Transport
Layer
1. Addressing
2. End-to-end connection management
3. Transparent data transfer between processes

## Slide 3: Transport Service
Connection oriented service
  3 phases
    connection set-up
    data transfer
    disconnect
Connectionless service
  Transfer of independent messages
Realization: transport entity
  Software and/or hardware
  Software part usually contained within the kernel (process, library)
1-2
3
4
5
Application
Layer
Transport
Entity
Network
Layer
Application
Layer
Transport
Entity
Network
Layer
Service Interface
Transport
Protocol
Port
IP: Message
TCP/IP 1. Port
2. IP address !!
ISO TSAP
(transport service access point)
Notes: Historically in Unix: socket = TSAP

## Slide 4: Transport Layer Function
Transport layer tasks
1-2
3
4
5
Network
Layer
Application
Transport
Layer
1-2
3
4
5
Network
Layer
Application
Transport
Layer
1. Addressing
2. End-to-end connection management
3. Transparent data transfer between processes
4. Quality of service options
  Error recovery
  Reliability
  Flow control
  Congestion control
Notes: tjenestekvalitet: korrektur av feil, pålitelighet, samt flytkontroll og metningskontroll – de siste krever litt mer forklaring

## Slide 5: Congestion and Flow Control
Opposite objectives
End-system
  Optimize its own throughput
  Possibly at the expense of other end-systems
Opposite objectives
Network
  Optimize overall throughput
Two different problems
  Receiver capacity
  Network capacity
Cannot be distinguished easily at all places
But should be differentiated
Transmission rate
adjustment
Network
Internal
congestion
Small receiver
capacity
Large receiver
capacity
Packet loss
Congestion
control
Flow
control

## Slide 6: Transport Layer Function
Transport protocols of TCP/IP protocol suite
  Services provided implicitly
TCP
UDP
SCTP
DCCP
Connection-oriented service
Connectionless service
Ordered
Reliable
Unordered
Unreliable
With congestion control
Without congestion control
Multicast support
Multihoming support
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Partially Ordered
X
Partially Reliable
X

## Slide 7: Transport Service: Terminology
Nesting of messages, packets, and frames
Layer
Transport
Network
Data link
Physical
Data Unit
Message, Packet
Packet
Frame
Bit/symbol (bitstream)
Message Payload
Packet Payload
Frame Payload
Message header
Packet header
Frame header
TCP/IP Message
ISO TPDU
(transport protocol data unit)
TCP name for Message Payload: Segment
UDP name for Message:
Datagram
Notes: Tanenbaum 6.1.2
Hvorfor har disse L4 pakker forskjellige navn?
Datagram er enkelt: det minner om telegram, som er en personlig melding, kort og avsluttet.
Men segment, dette høres ut som en brøkdel av noe større.

## Slide 8: Internet terminology
TCP sends a stream of bytes
  it doesn’t offer a packet service to the application layer
TCP content could be divided across multiple IPv4 packets (fragmentation)
  but then all content is destroyed with the loss of one IPv4 packet
  also, fragmentation in IPv6 is only allowed at the sender (using an option), where TCP can do it better
  so TCP splits its content into segments that fit into an L3 packet
hence normally message =packet
  and in everyday work: packet ≈ message or packet ≈ segment
  distinction from context

## Slide 9: Transport Protocols
UDP

## Slide 10: UDP - User Datagram Protocol
UDP is a simple transport protocol
  Unreliable
  Connectionless
  Message-oriented
UDP is mostly IP with short transport header
  De-/multiplexing
  Source and destination port
  Ports allow for dispatching of messages to receiver process

## Slide 11: UDP: Message Format
Source port
  Optional
  16 bit sender identification
  Response may be sent there
Destination port
  Receiver identification
Packet length
  In byte (including UDP header)
  Minimum: 8 (byte) i.e. header without data
Checksum
  Optional in IPv4
  Checksum of header and data for error detection
Destination Address
Source address
Time to live
Protocol
Header checksum
Identification
D
M
Fragment offset
Version
IHL
Type of service
Total length
PRE
ToS
Data
Options
Source port
Destination port
IP header
UDP header
Packet length
Checksum
Used for demultiplexing:
service address

## Slide 12: UDP: Message Format – Checksum
Purpose
  Error detection (header and data)
UDP checksum includes
  UDP header (checksum field initially set to 0)
  Data
  Pseudoheader
    Part of IP header
      source IP address
      destination IP address
      Protocol
      length of (UDP) data
    Allows to detect misdelivered UDP messages
Use of checksum optional
  i.e., if checksum contains only "0"s, it is not used
    Transmit 0xFFFF if calculated checksum is 0
Destination Address
Source address
00000000
Protocol=17
UDP segment length
Notes: Algorithm: One’s complement of sum of 16-bit halfwords in one’s complement arithmetic

## Slide 13: UDP: Ranges of Application
Suitable
  For simple client-server interactions, i.e. typically
    1 request packet from client to server
    1 response packet from server to client
  When delay is worse than packet loss and duplication
    Video conferencing
    IP telephony
    Gaming
Used by e.g.
  DNS: Domain Name Service ¹
  NTP: Network Time Protocol ¹
  SNMP: Simple Network Management Protocol
  BOOTP: Bootstrap protocol
  TFTP: Trivial File Transfer Protocol
  NFS: Network File System ¹
  RTP: Real-time Transport Protocol ¹
  ¹ can also be used with TCP
Notes: Benefits of UDP
  Needs very few resources (in endsystems, in each data unit), No connection establishment (hence, no overhead, faster transmission)
  Simple implementation possible (e.g. suitable for boot PROM), Applications can precisely control: Packet flow .... Error handling / reliability .... Timing
Problems of UDP
  No flow control: Packets can be lost because receiving application is too slow
  No congestion control: No reaction to network overload